## Slide 1: AD-FRQCVT1 Low Frequency Adapter for FMCOMM3 Initial Evaluation Results
Benjamin Sam, Charly El-Khoury
3/18/2015

## Slide 2: AD-FRQCVT1 Standalone Rx Conversion Gain
Chart: Conversion Gain Measurement
| 1 | 10 | 30 | 50 | 70 | 100
Gain | -7.7 | 13.1 | 14.8 | 13.6 | 12.9 | 11.4

## Slide 3: Standalone Rx P1dB
Chart: P1dB Measurement (Fin=70 MHz)
| -20 | -15 | -12 | -10 | -9 | -8 | -7 | -6 | -4 | -3
Pout | -7.1 | -2.3 | 0.7 | 2.6 | 3.55 | 4.47 | 5.29 | 5.86 | 6.26 | 6.19
SSG-1 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9
Gain | 12.9 | 12.7 | 12.7 | 12.6 | 12.55 | 12.47 | 12.29 | 11.86 | 10.26 | 9.19

## Slide 4: Standalone Tx Output Spectrum
Tx frequency set to 70 MHz
Fin=370 MHz, Pin=-15 dBm
Found Reference Spurs at +/-730 kHz

## Slide 5: System Evaluation: Tx Output
Output Level: adjustable with TX Ch2 Attenuation
  FTX = 25 MHz
  0 dB Attn => Po = +8.1 dBm
  80 dB Attn => Po = -73 dBm
Pout is flat to 1 dB from 20-100 MHz, but peaks up by 6 dB at 2 MHz, due to FRQCVT1 gain flatness
Rx setting changed from 1-100 MHz, no additional spur observed (<-85 dBm)
Rx input varied from 1-100 MHz, no additional spur observed

## Slide 6: System Evaluation: Tx Output
Output frequency is low by 1 MHz, with two spurs
  Set to 25 MHz, got 24, 25 & 26 MHz
2nd harmonics is 50 dB down
Came from AD9361 Tx Output, with Fo modulated by DDS
If DDS is turned off, only LO feedthrough remains (-50 dBm) at output of AD9361
FRQCVT1 output
25 MHz
AD9361 TX2 output
370 MHz